## Slide 1
I. DE MICHELIS, Associate Professor
University Of L’Aquila
Final Conference, 17/09/2020, Avezzano (Italy)
Experimental Results Achieved with BITMAPS

## Slide 2
LIFEBITMAPS PROJECT

## Slide 3
LIFEBITMAPS PROJECT
ONE OF THE KEY OBJECTIVE:
Demonstrate, at industrial scale, the feasibility/sustainability for TMAH treatment through an aerobic biodegradation of such toxic substance carried out by adapted microorganisms selected during the R&D phase.

## Slide 4
LIFEBITMAPS PROJECT

## Slide 5
LIFEBITMAPS PROJECT
pH | 12
TMAH | 2161 mg/L
N-NH4 | 7.4 mg/L
N-NO3 | < 0.15 mg/L
Dimethylamine (DMA) | < 0.05 mg/L
Average composition of WW1
Three run of experiments
Batch and Continuos mode
Different flowrate

## Slide 6
LIFEBITMAPS PROJECT
First Run
Trend of some parameters in the reactor R101

## Slide 7
LIFEBITMAPS PROJECT
First Run
Chart: R101
| 7 | 8 | 13 | 14
TMAH R101 | 567.35 | 769.24 | 36.42 | 42.96
DMA R101 | 71.236 | 7.1938 | 1.95 | 1.95
N-NH4 R101 | 86.5 | 107.5 | 180 | 185
NO3 R101 | 78.64 | 86.83 | 85.23 | 89.83

## Slide 8
LIFEBITMAPS PROJECT
Chart: R102
| 7 | 8 | 13 | 14
TMAH R102 | 1.4637 | 1.4637 | 3.7884 | 3.8819
DMA R102 | 0.39 | 0.39 | 0.39 | 0.09
N-NH4 R102 | 57.8 | 59.6 | 81 | 89.5
NO3 R102 | 510 | 494 | 616 | 667
Chart: R103
| 7 | 8 | 13 | 14
TMAH R103 | 0.293 | 0.293 | 0.806 | 0.916
DMA R103 | 0.178 | 0.178 | 0.178 | 0.178
N-NH4 R103 | 37.6 | 47.6 | 75 | 78.5
NO3 R103 | 610.24 | 550.81 | 670.66 | 717.75
TMAH and degradation products disappear. TMAH was completely degraded in the first biological reactor.
NO3 conc. increases: nitrification process, by which ammonia is oxidated to nitrate, happens

## Slide 9
LIFEBITMAPS PROJECT
Second Run
Trend of some parameters in the reactor R101
Wash-Out

## Slide 10
LIFEBITMAPS PROJECT
Residence time is insufficient to allow microorganisms duplication
Optimal flowrate value: 5L/h

## Slide 11
LIFEBITMAPS PROJECT
Time [h] | R101 | R102 | R013
48 | 7.53% | 45.10% | 55.38%
168 | 61.46% | 96.47% | 99.97%
192 | 55.48% | 90.82% | 99.02%
TMAH Degradation yields (%) for each reactor (5L/h)
Chart: TMAH concentration [mg/L]
R101 | 0 | 470 | 507 | 633
R102 | 0 | 37.1 | 18.6 | 58.1
R103 | 0 | 2.84 | 0.05 | 2.04
Material balance for each reactor:

## Slide 12
LIFEBITMAPS PROJECT
Third Run
Trend of TMAH at 5L/h
Chart: TMAH
| 96 | 192 | 288 | 360 | 432 | 504 | 600 | 672 | 840
R101 | 0.483 | 283.459 | 0.412 | 0.357 | 88.612 | 199.7 | 1253.75 | 1354.82 | 1016.72
R102 | 0.119 | 0.317 | 0.33 | 0.567 | 0.619 | 6.11 | 0.38 | 80.18 | 17.94
R103 | 8.688 | 10.411 | 0.313 | 0.353 | 0.119 | 5.999 | 4.33 | 20.34 | 10.6
failure

## Slide 13
LIFEBITMAPS PROJECT
Third Run
Chart: TMAH
| 96 | 192 | 288 | 360 | 432 | 504 | 600 | 672 | 840
R101 | 0.483 | 283.459 | 0.412 | 0.357 | 88.612 | 199.7 | 1253.75 | 1354.82 | 1016.72
R102 | 0.119 | 0.317 | 0.33 | 0.567 | 0.619 | 6.11 | 0.38 | 80.18 | 17.94
R103 | 8.688 | 10.411 | 0.313 | 0.353 | 0.119 | 5.999 | 4.33 | 20.34 | 10.6
Chart: pH
| 43605 | 43606 | 43607 | 43608 | 43609 | 43610 | 43611 | 43612 | 43613 | 43614 | 43615 | 43616 | 43617 | 43618 | 43619 | 43620 | 43621 | 43623 | 43624 | 43625 | 43626 | 43627 | 43629 | 43630 | 43631 | 43632 | 43633 | 43634 | 43635 | 43636 | 43637 | 43638 | 43639 | 43640 | 43641 | 43642 | 43643
R101 | 6.1154 | 5.981 | 6.4452 | 6.3101 | 5.9034 | 6.492 | 6.5634 | 6.5153 | 6.5882 | 5.8725 | 5.349 | 5.0594 | 4.3728 | 4.0914 | 4.0059 | 3.9948 | 4.0536 | 6.3464 | 6.6932 | 6.6816 | 6.7368 | 6.7028 | 6.7332 | 6.7154 | 6.6463 | 6.7153 | 6.7096 | 6.698 | 6.7204 | 6.7332 | 6.6667 | 6.6991 | 6.7214 | 6.7166 | 6.719 | 6.71 | 6.7096
R102 | 5.8384 | 5.6411 | 5.3683 | 5.1701 | 5.1097 | 5.0741 | 5.0111 | 4.958 | 4.9193 | 4.9523 | 5.0268 | 4.995 | 4.8495 | 4.7411 | 4.7559 | 4.7019 | 5.1966 | 5.3155 | 5.0701 | 4.6886 | 4.5909 | 4.2039 | 3.9772 | 3.9432 | 3.877 | 3.9126 | 3.9167 | 3.922 | 3.9256 | 4.0577 | 4.0763 | 4.2328 | 4.4459 | 4.1433 | 4.1649 | 4.3606 | 4.4159
R103 | 7.6886 | 7.6223 | 7.5589 | 7.4436 | 7.4605 | 7.4052 | 7.3 | 7.0975 | 6.6565 | 5.7519 | 5.2239 | 5.0415 | 4.9743 | 4.9222 | 4.896 | 4.9877 | 5.2561 | 6.3275 | 6.5495 | 6.6436 | 6.7703 | 6.7644 | 6.7659 | 6.7316 | 6.6595 | 6.8833 | 6.7895 | 6.7607 | 6.7938 | 6.6694 | 6.6794 | 6.7706 | 6.7668 | 6.7352 | 6.6857 | 6.6113 | 6.4987
failure
It is possible to justified biological system failure by microorganism suffering due to carbon deficiency. During the tests no additional source of carbon was added. It is possible to hypothesize that in the initial phase the system is not affected by the lack of carbon

## Slide 14
LIFEBITMAPS PROJECT
Chart: R101- TMAH
| 0 | 72 | 192 | 216
october 2018 | 0 | 470 | 507 | 633
june 2019 | 0.483 | 283.459 | 0.412 | 0.357 | 88.612 | 199.7 | 6.72
Second Run vs Third Run
despite the thermostat control system, the average temperature in biological reactors, during the 2018 tests, was below 20 ° C, while in tests conducted in June 2019 the temperature was on average around 25 ° C (optimal temperature according to laboratory data)

## Slide 15
LIFEBITMAPS PROJECT
Chart: TMAH data vs TMAH calculated
| 96 | 192 | 288 | 360 | 432 | 504 | 600
R103 | 8.688 | 10.411 | 0.313 | 0.353 | 0.119 | 5.999 | 4.33
R102 | 0.119 | 0.317 | 0.33 | 0.567 | 0.619 | 6.11 | 0.38
R101 | 0.483 | 283.459 | 0.412 | 0.357 | 88.612 | 199.7 | 1253.75
 | TMAH Removal Yield |  | 
Time (h) | R101 | R102 | R103
96 | 99,9% | 99,9% | 76,2%
192 | 78,5% | 99,9% | 94,6%
288 | 100,0% | 100,0% | 99,9%
360 | 100,0% | 100,0% | 99,9%
432 | 95,1% | 100,0% | 100,0%
504 | 89,4% | 99,6% | 99,4%
600 | 99,7% | 99,7% | 99,5%
TMAH removal yield with respect to theoretical value

## Slide 16
LIFEBITMAPS PROJECT
Lfoundry depurator tests

## Slide 17
LIFEBITMAPS PROJECT
Lfoundry depurator tests

## Slide 18
LIFEBITMAPS PROJECT
SEZ treatment
Date | pH |  | Volume of wastewater, L | Reagent consumption, kg | 
 | initial | final |  | Al2(SO4)3 | Ca(OH)2, 16%
24/09/18 | 1.5 | 4.5 | 102.14 | 3.00 | 200.0
8/11/18 | 1.5 | 4.9 | 99.10 | 3.04 | 95.4
15/11/18 | 1.5 | 5.2 | 101.3 | 3.00 | 144.3
Reagent consumption for SEZ treatment
Date | Waste water |  | Precipitate, % |  |  |  |  | 
 | F, mg/L |  | Water content | Ca | Al | Na | P | S
 | initial | final |  |  |  |  |  | 
24/09/18 | 20600 | 7.8 | 65.5 | 62.1 | 3.5 | 6.8 | 19.2 | 7.7
8/11/18 | 16400 | 9.6 | 56.4 | 58.5 | 4.6 | 6.8 | 19.4 | 10.1
15/11/18 | 17500 | 5.1 | 55.7 | 62.4 | 2.1 | 7.7 | 23.4 | 3.8
Wastewater SEZ parameters before and after treatment

## Slide 19
LIFEBITMAPS PROJECT
BOE treatment
Date | pH |  | Volume of wastewater, L | Reagent consumption, kg | 
 | initial | final |  | Al2(SO4)3 | Ca(OH)2, 16%
04/10.18 | 4.8 | 11.8 | 100 | 4.0 | 182.8
15/10/18 | 5.3 | 9.2 | 105 | 4.0 | 120
31/10/18 | 5.4 | 9.9 | 94.3 | 4.0 | 89
Reagent consumption for BOE treatment
Wastewater BOE parameters before and after treatment
Date | Wastewater |  |  |  |  | Precipitate, % |  |  |  | 
 | F, mg/L |  | PO4, mg/L |  | NO3, mg/L | Water content | Ca | Al | P | Na
 | initial | final | initial | final |  | Water content | Ca | Al | P | Na
04/10.18 | 97 | 5.3 | 245 | 0 | 29000 | 48.1 | 91.7 | 1.9 | 4.8 | 1.1
15/10/18 | 418 | 4.6 | 333 | 0 | 762000 | 51.2 | 90.4 | 2.5 | 5.2 | 1.2
31/10/18 | 25700 | 9.9 | 380 | 0 | 16500 | 53.4 | 90.9 | 2.2 | 5.0 | 1.4

## Slide 20
LIFEBITMAPS PROJECT
Conclusions:
data showed that using a loading of TMAH solution of 5 L/h and after 192 h of reaction it has been possible to reach 55.48%, 90.82% and 99.02% of removal in R101, R102 and R103, respectively.
DMA appears after 48 h and it is degraded by bacteria in 192 h that product ammonium.
nitrification process was more relevant in the last bioreactor.
the 5 ° C increase in temperature improves the kinetics of the system

## Slide 21
LIFEBITMAPS PROJECT
Conclusions:
about system biology, changes in pH and nutrient inlet causes the selection of different species into the reactor;
changes in operational parameters, such as variation to inlet/outlet amount per hour, should be made with extreme caution
an automated pH controller should be considered, to maintain acidity to optimal levels, avoiding dangerous shifts in microbial community.

## Slide 22
LIFEBITMAPS PROJECT
Conclusions:
SEZ and BOE: both effluents can be treated by the addition of lime and aluminium sulphate as precipitation coadjuvant;
fluoride removal yield is around 99% for both effluents;
lime consumption depends from initial composition of the effluent and from the age of the lime.

## Slide 23
Thank You very much for your attention !
This Project receives funding form the European Union Life Programme Under Grant Agreement N. LIFE 15 ENV/IT 000332.